## Slide 1
Design and Simulation of a Smart Parking Slot Availability and Entry Control System
DDCA PROJECT • Mathematical Theme: LOGIC GATES
AKHILA — 2620030655
SARADA — 2620030660
PAVAN — 2620030658
KRITHIKA — 2620030664
Guide: ____________________ | Department: CSE | KLH Bachupally | Academic Year: 2026–27

## Slide 2
1. Introduction
Why a smart parking control system is useful
Parking becomes difficult when drivers cannot quickly know whether a slot is available.
• The system represents each parking slot using a binary status.
• Logic gates process slot status and vehicle-arrival information.
• The entry gate opens only when a vehicle arrives and a slot is available.
• A full indicator turns ON when both slots are occupied.
• The complete design can be simulated and verified in Logisim.
S1
Slot 1
S2
Slot 2
V
Vehicle
Binary inputs → logic gates → control outputs
DDCA • Smart Parking System
2

## Slide 3
2. Problem Statement
The control problem our circuit solves
Problem
• A vehicle may arrive when all parking slots are occupied.
• The gate must not open unless a slot is available.
• The system must clearly indicate the full condition.
• Manual checking can cause delays and incorrect entry decisions.
Need for the proposed solution
• Simple binary representation of real-world slot states.
• Deterministic decision making using Boolean logic.
• Safe entry control: Gate_Open = 0 when parking is full.
• Easy implementation and testing in Logisim.
Key idea: convert parking conditions into a small, verifiable digital circuit.
DDCA • Smart Parking System
3

## Slide 4
3. Objectives
Specific goals of the DDCA project
01
Detect slot availability
Determine whether both slots are empty.
02
Control entry
Open the gate only for an arriving vehicle when space exists.
03
Detect full parking
Turn ON the full indicator when both slots are occupied.
04
Use Boolean logic
Implement the design using NOT and AND gates.
05
Simulate & verify
Test every input combination using Logisim and a truth table.
06
Document progress
Maintain the circuit and implementation work in GitHub.
DDCA • Smart Parking System
4

## Slide 5
4. Literature Survey / Existing System
From manual checking to logic-based automation
Approach
How it works
Limitation
Manual parking check
Driver/security staff checks slot availability.
Slow and human-dependent.
Simple slot indicator
Sensors/indicators show individual occupied slots.
Does not automatically control entry.
Rule-based controller
Predefined conditions decide whether entry is allowed.
Can become complex as conditions increase.
Proposed DDCA circuit
Boolean gates combine slot states and vehicle arrival.
Small design; optimized for a 2-slot demonstration.
Design decision: keep the logic transparent and easy to prove with a truth table.
DDCA • Smart Parking System
5

## Slide 6
5. Proposed System
Boolean specification of the smart parking controller
Availability
A = ¬S1 ∧ ¬S2
Both slots must be empty
Gate control
Gate_Open = V ∧ A
Vehicle + available space
Full detection
Parking_Full = S1 ∧ S2
Both slots occupied
Inputs
S1 = 0 empty / 1 occupied
S2 = 0 empty / 1 occupied
V = 1 vehicle arrived
DDCA • Smart Parking System
6

## Slide 7
6. System Architecture / Block Diagram
Signal flow from parking slots to entry control
S1
Slot 1 Status
S2
Slot 2 Status
SLOT DETECTION
¬S1 ∧ ¬S2
ENTRY CONTROL
V ∧ Available
GATE OPEN
1 = Open
V
Vehicle
FULL DETECTOR
S1 ∧ S2
PARKING FULL
1 = Full
Two independent outputs: entry permission + full status
DDCA • Smart Parking System
7

## Slide 8
7. Methodology / Implementation
Clear gate-by-gate Logisim implementation
A. SLOT AVAILABILITY + ENTRY CONTROL
S1
0 = Empty 1 = Occupied
S2
0 = Empty 1 = Occupied
NOT
NOT
¬S1
¬S2
AND
SLOT AVAILABLE
A = ¬S1 ∧ ¬S2
V
1 = Vehicle Arrived
AND
GATE OPEN
Gate_Open = V ∧ A
Gate_Open
1 = Gate Opens
B. PARKING FULL DETECTION
S1
S2
AND
Parking_Full = 1
Logic used: NOT + AND | Every block maps directly to the Boolean equation.
8

## Slide 9
8. Results and Discussion
Truth-table verification of the Boolean design
S1
S2
V
Available A
Gate_Open
Parking_Full
0
0
0
1
0
0
0
0
1
1
1
0
0
1
0
0
0
0
0
1
1
0
0
0
1
0
0
0
0
0
1
0
1
0
0
0
1
1
0
0
0
1
1
1
1
0
0
1
Expected observations
• Gate_Open = 1 only for S1=0, S2=0, V=1.
• Gate_Open stays 0 if no vehicle arrives.
• Parking_Full = 1 whenever S1=1 and S2=1.
• The full signal does not depend on V.
• Every input combination has a deterministic output.
This truth table becomes the test plan for the Logisim circuit.
DDCA • Smart Parking System
9

## Slide 10
9. Conclusion & Project Implementation
What the project achieves and how the team will submit it
Conclusion
• A 2-slot smart parking controller was specified using Boolean logic.
• NOT gates detect empty slots; AND gates implement availability, entry control, and full detection.
• The truth table provides a complete correctness check for the design.
• The circuit is compact, transparent, and directly implementable in Logisim.
Required project deliverables
01
Project PPT
Presentation of the complete project.
02
Circuit file (.circ)
Logisim implementation of the logic.
03
GitHub repository
Each student commits and pushes their actual work.
Recommended GitHub flow: clone → create branch → implement → commit → push → merge/pull request.
DDCA • Smart Parking System
10

## Slide 11
THANK YOU
Design and Simulation of a Smart Parking Slot Availability and Entry Control System
AKHILA • SARADA • PAVAN • KRITHIKA
DDCA Project | KLH Bachupally | 2026–27
DDCA • Smart Parking System
11